## Slide 1: VLSI Finite-State Machines (FSM)
Cairo University
Faculty of Engineering
Computer Engineering Department
Sandra Wahid

## Slide 2: FSM
If a system transits between finite number of internal states, then finite state machines (FSM) can be used to design the system.
The FSM can change from one state to another in response to some inputs; the change from one state to another is called a transition.
An FSM is defined by a list of its states, its initial state, and the inputs that trigger each transition.

## Slide 3: Example

## Slide 4: FSM Behavior Types
FSM can be divided into two different behavior types:
  Mealy machines
  Moore machines

## Slide 5: FSM States in VHDL

## Slide 6: Example: Parity checker
Serial input string
  OUT=1 if odd # of 1s in input
  OUT=0 if even # of 1s in input
Input/output:

## Slide 7: Mealy Machine: 2 blocks
A general model of a Mealy machine consists of:
  a combinatorial network which generates the outputs and the next state,
  and a state register which holds the present state as shown below. The state register is normally modeled as D flip-flops. The state register must be sensitive to a clock edge

## Slide 8: Mealy Machine: 2 blocks
Even: S0
Odd: S1

## Slide 9: Mealy Machine: 3 blocks

## Slide 10: Moore Machine: 3 blocks
A general model of a Moore machine consists of:
  combinatorial network which generates the outputs,
  combinatorial network which generates the next state
  and a state register which holds the present state as shown below. The state register is normally modeled as D flip-flops. The state register must be sensitive to a clock edge

## Slide 11: Moore Machine: 3 blocks
Even: S0
Odd: S1

## Slide 12
Thank You